## Slide 1
Processor Architecture I: ISA & Logic Design Introduction to Computer Systems 9th Lecture, Oct 15, 2026

## Slide 2: Part A Instruction Set Architecture

## Slide 3: Instruction Set Architecture
ISA:
  Processor state
    Registers, memory
  Instructions
    addq, pushq, ret, …
Contract between HW and SW:
  Above: how SW programs?
  Below: how HW implements?
ISA
Compiler
OS
CPU
Design
Circuit
Design
Chip
Layout
Application
Program

## Slide 4: Y86-64 processor state
ZF
SF
OF
  Program Registers (diff)
    15 64-bits registers (omit %r15).
  Single-digit condition Codes (diff)
    ZF: Zero SF:Negative OF: Overflow
  Program Counter (same)
  Program Status (same)
  Memory (same)
    Little-endian
RF: Program registers
CC: Condition codes
PC
DMEM: Memory
Stat: Program status
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%rax
%rcx
%rdx
%rbx
%rsp
%rbp
%rsi
%rdi

## Slide 5: Encoding Y86-64 Instructions
Remember: instruction is stored as binary data in memory
Format: 1–10 bytes
    First byte: instruction type
    Second byte: function (specific instructions within one type)
    Starting from third byte: oprands (memory addresses, registers)

## Slide 6: Y86-64 Instructions #1
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9

## Slide 7: Y86-64 Instruction Set #2
0
1
2
3
4
5
6
7
8
9
V
D
D
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
rmmovq rA, D(rB)
4
0
rA
rB
mrmovq D(rB), rA
5
0
rA
rB
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
rrmovq
2
0
cmovle
2
1
cmovl
2
2
cmove
2
3
cmovne
2
4
cmovge
2
5
cmovg
2
6

## Slide 8: Y86-64 Instruction Set #3
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
addq
6
0
subq
6
1
andq
6
2
xorq
6
3

## Slide 9: Y86-64 Instruction Set #4
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
jmp
7
0
jle
7
1
jl
7
2
je
7
3
jne
7
4
jge
7
5
jg
7
6

## Slide 10: Y86-64 Instructions
Format: 1–10 bytes
    First byte: instruction type
    Second byte: function (specific instructions within one type)
    Starting from third byte: oprands (memory addresses, registers)
Each register has 4-bit ID (almost same as x86)
Except for 0xF indicates “no register”
  Use in our hardware design
%rax
%rcx
%rdx
%rbx
0
1
2
3
%rsp
%rbp
%rsi
%rdi
4
5
6
7
%r8
%r9
%r10
%r11
8
9
A
B
%r12
%r13
%r14
No Register
C
D
E
F

## Slide 11: Instruction Example
Addition Instruction
  e.g., addq %rax,%rsi Encoding: 60 06
addq rA, rB
6
0
rA
rB
Encoded Representation

## Slide 12: Move Operations
  Like the x86-64 movq instruction with simpler addressing mode
rrmovq rA, rB
2
0
Register  Register
Immediate  Register
irmovq V, rB
F
rB
3
0
V
Register  Memory
rmmovq rA, D(rB)
4
0
rA
rB
D
Memory  Register
mrmovq D(rA), rB
5
0
rB
rA
D
rA
rB

## Slide 13: Move Instruction Examples
irmovq $0xabcd, %rdx
movq $0xabcd, %rdx
30 f2 cd ab 00 00 00 00 00 00
X86-64
Y86-64
Encoding:
rrmovq %rsp, %rbx
movq %rsp, %rbx
20 43
mrmovq -12(%rbp),%rcx
movq -12(%rbp),%rcx
50 15 f4 ff ff ff ff ff ff ff
rmmovq %rsi,0x41c(%rsp)
movq %rsi,0x41c(%rsp)
40 64 1c 04 00 00 00 00 00 00
Encoding:
Encoding:
Encoding:

## Slide 14: Conditional Move Instructions
  Refer to generically as “cmovXX”
  Variants of rrmovq instruction
  Encodings differ only by “function code”
  Based on values of condition codes
    cmovne performs when ZE is clear
rrmovq rA, rB
Move Unconditionally
cmovle rA, rB
Move When Less or Equal
cmovl rA, rB
Move When Less
cmove rA, rB
Move When Equal
cmovne rA, rB
Move When Not Equal
cmovge rA, rB
Move When Greater or Equal
cmovg rA, rB
Move When Greater
2
0
rA
rB
2
1
rA
rB
2
2
rA
rB
2
3
rA
rB
2
4
rA
rB
2
5
rA
rB
2
6
rA
rB

## Slide 15: Jump Instructions
  Same as x86-64 counterparts
  Refer to generically as “jXX”
  Encodings differ only by “function code” fn
  Based on values of condition codes
    je 0x100 only jumps if ZF is set
jXX Dest
7
fn
Jump (Conditionally)
Dest

## Slide 16: Jump Instructions
jmp Dest
7
0
Jump Unconditionally
Dest
jle Dest
7
1
Jump When Less or Equal
Dest
jl Dest
7
2
Jump When Less
Dest
je Dest
7
3
Jump When Equal
Dest
jne Dest
7
4
Jump When Not Equal
Dest
jge Dest
7
5
Jump When Greater or Equal
Dest
jg Dest
7
6
Jump When Greater
Dest

## Slide 17: Y86-64 Program Stack (same as x86)
  Supporting procedure calls
  Stack top indicated by %rsp
  Stack grows toward lower addresses
%rsp
•
•
•
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 18: Stack Operations (same as x86)
  Decrement %rsp by 8
  Store word from rA to memory at %rsp
  Read word from memory at %rsp to register rA
  Increment %rsp by 8
pushq rA
A
0
rA
F
popq rA
B
0
rA
F

## Slide 19: Function Call and Return (same as x86)
  Push address of next instruction onto stack, and go to dest
  Pop value from stack as address for next instruction
call Dest
8
0
Dest
ret
9
0

## Slide 20: Miscellaneous Instructions
  Don’t do anything
  Stop executing instructions; put the processor into low-power mode
  We will use it to stop the simulator
nop
1
0
halt
0
0

## Slide 21: Status Conditions
Mnemonic | Code
ADR | 3
Mnemonic | Code
INS | 4
Mnemonic | Code
HLT | 2
Mnemonic | Code
AOK | 1
  Normal operation
  Halt instruction encountered
  Bad address (either instruction or data) encountered
  Invalid instruction encountered
Desired Behavior
  If AOK, keep going
  Otherwise, stop program execution

## Slide 22: Writing Y86-64 Code
Coding Example
  Find number of elements in null-terminated list
    int len1(long * a);
5043
6125
7395
0
a
 3

## Slide 23: x86-64 Code
Problem
  Can we translate this to Y86?
/* Find number of elements in
null-terminated list */
long len(long * a)
{
long len;
for (len = 0; a[len]; len++)
;
return len;
}
L3:
addq $1,%rax
cmpq $0, (%rdi,%rax,8)
jne L3

## Slide 24: Y86-64 Code Generation Example #3
len:
irmovq $1, %r8 # Constant 1
irmovq $8, %r9 # Constant 8
irmovq $0, %rax # len = 0
mrmovq (%rdi), %rdx # val = *a
andq %rdx, %rdx # Test val
je Done # If zero, goto Done
Loop:
addq %r8, %rax # len++
addq %r9, %rdi # a++
mrmovq (%rdi), %rdx # val = *a
andq %rdx, %rdx # Test val
jne Loop # If !0, goto Loop
Done:
ret
Register | Use
%rdi | a
%rax | len
%rdx | val
%r8 | 1
%r9 | 8

## Slide 25: Part B Logic Design

## Slide 26: Digital Signals
  Use voltage thresholds to extract 0 and 1
Voltage
Time
0
1
0

## Slide 27: Computing with Logic Gates
  Outputs are Boolean functions of inputs

## Slide 28: Bit Equality
  Generate 1 if a and b are equal
Bit equal
a
b
out

## Slide 29: Word Equality
  64-bit word size
b63
Bit equal
a63
eq63
b62
Bit equal
a62
eq62
b1
Bit equal
a1
eq1
b0
Bit equal
a0
eq0
Eq
=
B
A
Eq
Word-Level Representation

## Slide 30: Bit-Level Multiplexor
  Output a when s=1, b when s=0
Bit MUX
b
s
a
out

## Slide 31: Word Multiplexor
  Select input word A or B depending on control signal s
b63
s
a63
out63
b62
a62
out62
b0
a0
out0
Word-Level Representation
s
B
A
Out
MUX

## Slide 32: Arithmetic Logic Unit
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
  Control signal selects function computed
    Corresponding to 4 arithmetic/logical operations in Y86-64
A
L
U
Y
X
X + Y
0
A
L
U
Y
X
X - Y
1
A
L
U
Y
X
X & Y
2
A
L
U
Y
X
X ^ Y
3
A
B
A
B
A
B
A
B

## Slide 33: Registers
  Stores data with latches
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
i7
i6
i5
i4
i3
i2
i1
i0
o7
o6
o5
o4
o3
o2
o1
o0
Clock
Structure

## Slide 34: Register file
  Register file
    Holds values of program registers
    %rax, %rsp, etc.
    Register identifier serves as address
      ID 15 (0xF) implies no read or write performed
  Multiple Ports
    Can read and/or write multiple registers
Register
file
A
B
W
dstW
srcA
valA
srcB
valB
valW
Read ports
Write port
Clock

## Slide 35: Memory is the same
Memory
A
B
W
addrA
valA
addrB
valB
Ports
Clock
addrW
valW
Write port

## Slide 36
Timing

## Slide 37: Computing with Logic Gates
  Outputs are Boolean functions of inputs
  Respond continuously to changes in inputs
    With some, small delay
Voltage
Time
a
b
a && b
Rising Delay
Falling Delay

## Slide 38: Combinational Circuits
Network of Logic Gates
  Continously responds to changes on primary inputs
  Primary outputs become (after some delay) Boolean functions of primary inputs
Network
Primary
Inputs
Primary
Outputs

## Slide 39: Register Operation
  Stores data bits
  Acts as barrier between input and output
  As clock rises, loads input
State = x
Rising
clock

Output = x
Input = y
x

State = y
Output = y
y

## Slide 40: Register File Timing
Reading
  Like combinational logic
  Output data generated based on input address
    After some delay
Writing
  Update only as clock rises
Register
file
A
B
srcA
valA
srcB
valB
y
2
Register
file
W
dstW
valW
Clock
x
2
Rising
clock


Register
file
W
dstW
valW
Clock
y
2
x
2
x
2

## Slide 41: State Machine Example
  Accumulator circuit
  Load or accumulate on each cycle
Comb. Logic
A
L
U
0
Out
MUX
0
1
Clock
In
Load
x0
x1
x2
x3
x4
x5
x0
x0+x1
x0+x1+x2
x3
x3+x4
x3+x4+x5
Clock
Load
In
Out

## Slide 42: Hardware Control Language
  Simplified hardware description language, similar to C
Data Types
  bool:
    a, b, c, …
  int:
    A, B, C, …
    Does not specify word size---bytes, 64-bit words, …
Statements
  bool a = bool-expr ;
  int A = int-expr ;

## Slide 43: HCL Operations
  Classify by type of value returned
Boolean Expressions
  Logic Operations
    a && b, a || b, !a
  Word Comparisons
    A == B, A != B, A < B, A <= B, A >= B, A > B
  Set Membership
    A in { B, C, D }
      Same as A == B || A == C || A == D
Word Expressions
  Case expressions
    [ a : A; b : B; c : C ]
    Evaluate test expressions a, b, c, … in sequence
    Return word expression A, B, C, … for first successful test

## Slide 44: Bit Equality
  Generate 1 if a and b are equal
Hardware Control Language (HCL)
  Very simple hardware description language, similar to C
  We’ll use it to describe control logic for processors
Bit equal
a
b
out
bool out = (a&&b)||(!a&&!b)
HCL Expression

## Slide 45: Bit-Level Multiplexor
  Output a when s=1, b when s=0
Bit MUX
b
s
a
out
bool out = (s&&a)||(!s&&b)
HCL Expression

## Slide 46: Word Equality
  64-bit word size
b63
Bit equal
a63
eq63
b62
Bit equal
a62
eq62
b1
Bit equal
a1
eq1
b0
Bit equal
a0
eq0
Eq
=
B
A
Eq
Word-Level Representation
bool Eq = (A == B)
HCL Representation

## Slide 47: Word Multiplexor
  Select input word A or B depending on control signal s
Word-Level Representation
HCL Representation
b63
s
a63
out63
b62
a62
out62
b0
a0
out0
int Out = [
s : A;
1 : B;
];
s
B
A
Out
MUX

## Slide 48: HCL Examples
  Find minimum of three input words
A
Min3
MIN3
B
C
int Min3 = [
A < B && A < C : A;
B < A && B < C : B;
1 : C;
];
D0
D3
Out4
s0
s1
MUX4
D2
D1
  Select one of 4 inputs based on two control bits
int Out4 = [
!s1&&!s0: D0;
!s1 : D1;
!s0 : D2;
1 : D3;
];
Minimum of 3 Words
4-Way Multiplexor

## Slide 49: Summary
Computation
  Performed by combinational logic
  Computes Boolean functions
  Continuously reacts to input changes
Storage
  Registers
    Hold single words
    Loaded as clock rises
  Random-access memories
    Hold multiple words
    Possible multiple read or write ports
    Read word when address input changes
    Write word as clock rises

## Slide 50: Jump Instructions
  Refer to generically as “jXX”
  Encodings differ only by “function code” fn
  Based on values of condition codes
  Same as x86-64 counterparts
  Encode full destination address
    Unlike PC-relative addressing seen in x86-64
jXX Dest
7
fn
Jump (Conditionally)
Dest

## Slide 51: Y86-64 Sample Program Structure #1
  Program starts at address 0
  Must set up stack
  Must initialize data
init: # Initialization
. . .
call Main
halt
.align 8 # Program data
array:
. . .
Main: # Main function
. . .
call len . . .
len: # Length function
. . .
.pos 0x100 # Placement of stack
Stack:

## Slide 52: Y86-64 Program Structure #2
  Program starts at address 0
  Must set up stack
  Must initialize data
  Can use symbolic names
init:
# Set up stack pointer
irmovq Stack, %rsp
# Execute main program
  call Main
  # Terminate
  halt
# Array of 4 elements + terminating 0
.align 8
Array:
.quad 0x000d000d000d000d
  .quad 0x00c000c000c000c0
.quad 0x0b000b000b000b00
.quad 0xa000a000a000a000
.quad 0

## Slide 53: Y86-64 Program Structure #3
Set up call to len
  Follow x86-64 procedure conventions
  Push array address as argument
Main:
irmovq array,%rdi
# call len(array)
call len
ret

## Slide 54: Assembling Y86-64 Program
  Generates “object code” file len.yo
    Actually looks like disassembler output
  unix> yas len.ys
  0x054: | len:
  0x054: 30f80100000000000000 | irmovq $1, %r8 # Constant 1
  0x05e: 30f90800000000000000 | irmovq $8, %r9 # Constant 8
  0x068: 30f00000000000000000 | irmovq $0, %rax # len = 0
  0x072: 50270000000000000000 | mrmovq (%rdi), %rdx # val = *a
  0x07c: 6222 | andq %rdx, %rdx # Test val
  0x07e: 73a000000000000000 | je Done # If zero, goto Done
  0x087: | Loop:
  0x087: 6080 | addq %r8, %rax # len++
  0x089: 6097 | addq %r9, %rdi # a++
  0x08b: 50270000000000000000 | mrmovq (%rdi), %rdx # val = *a
  0x095: 6222 | andq %rdx, %rdx # Test val
  0x097: 748700000000000000 | jne Loop # If !0, goto Loop
  0x0a0: | Done:
  0x0a0: 90 | ret

## Slide 55: Simulating Y86-64 Program
  Instruction set simulator
    Computes effect of each instruction on processor state
    Prints changes in state from original
  unix> yis len.yo
  Stopped in 33 steps at PC = 0x13. Status 'HLT', CC Z=1 S=0 O=0
  Changes to registers:
  %rax: 0x0000000000000000 0x0000000000000004
  %rsp: 0x0000000000000000 0x0000000000000100
  %rdi: 0x0000000000000000 0x0000000000000038
  %r8: 0x0000000000000000 0x0000000000000001
  %r9: 0x0000000000000000 0x0000000000000008
  Changes to memory:
  0x00f0: 0x0000000000000000 0x0000000000000053
  0x00f8: 0x0000000000000000 0x0000000000000013

## Slide 56: CISC Instruction Sets
  Complex Instruction Set Computer
  IA32 is example
Stack-oriented instruction set
  Use stack to pass arguments, save program counter
  Explicit push and pop instructions
Arithmetic instructions can access memory
  addq %rax, 12(%rbx,%rcx,8)
    requires memory read and write
    Complex address calculation
Condition codes
  Set as side effect of arithmetic and logical instructions
Philosophy
  Add instructions to perform “typical” programming tasks

## Slide 57: RISC Instruction Sets
  Reduced Instruction Set Computer
  Internal project at IBM, later popularized by Hennessy (Stanford) and Patterson (Berkeley)
Fewer, simpler instructions
  Might take more to get given task done
  Can execute them with small and fast hardware
Register-oriented instruction set
  Many more (typically 32) registers
  Use for arguments, return pointer, temporaries
Only load and store instructions can access memory
  Similar to Y86-64 mrmovq and rmmovq
No Condition codes
  Test instructions return 0/1 in register

## Slide 58: MIPS Registers

## Slide 59: MIPS Instruction Examples
Op
Ra
Rb
Offset
Op
Ra
Rb
Rd
Fn
00000
R-R
Op
Ra
Rb
Immediate
R-I
Load/Store
addu $3,$2,$1 # Register add: $3 = $2+$1
addu $3,$2, 3145 # Immediate add: $3 = $2+3145
sll $3,$2,2 # Shift left: $3 = $2 << 2
lw $3,16($2) # Load Word: $3 = M[$2+16]
sw $3,16($2) # Store Word: M[$2+16] = $3
Op
Ra
Rb
Offset
Branch
beq $3,$2,dest # Branch when $3 = $2

## Slide 60: CISC vs. RISC
Original Debate
  Strong opinions!
  CISC proponents---easy for compiler, fewer code bytes
  RISC proponents---better for optimizing compilers, can make run fast with simple chip design
Current Status
  For desktop processors, choice of ISA not a technical issue
    With enough hardware, can make anything run fast
    Code compatibility more important
  x86-64 adopted many RISC features
    More registers; use them for argument passing
  For embedded processors, RISC makes sense
    Smaller, cheaper, less power
    Most cell phones use ARM processor

## Slide 61: Summary
Y86-64 Instruction Set Architecture
  Similar state and instructions as x86-64
  Simpler encodings
  Somewhere between CISC and RISC
How Important is ISA Design?
  Less now than before
    With enough hardware, can make almost anything go fast

## Slide 62: Overview of Logic Design
Fundamental Hardware Requirements
  Communication
    How to get values from one place to another
  Computation
  Storage
Bits are Our Friends
  Everything expressed in terms of values 0 and 1
  Communication
    Low or high voltage on wire
  Computation
    Compute Boolean functions
  Storage
    Store bits of information

## Slide 63: Digital Signals
  Use voltage thresholds to extract discrete values from continuous signal
  Simplest version: 1-bit signal
    Either high range (1) or low range (0)
    With guard range between them
  Not strongly affected by noise or low quality circuit elements
    Can make circuits simple, small, and fast
Voltage
Time
0
1
0

## Slide 64: Additional Slides

## Slide 65: Storing 1 Bit
Bistable Element
Q+
Q–
q
!q
q = 0 or 1
Vin
V1
V2

## Slide 66: Storing 1 Bit (cont.)
Bistable Element
Q+
Q–
q
!q
q = 0 or 1
Vin
V1
V2
Vin
V1
V2
Vin = V2
Stable 0
Stable 1
Metastable

## Slide 67: Physical Analogy
Stable 0
Stable 1
Metastable
.
Stable left
.
Stable right
.
Metastable

## Slide 68: Storing and Accessing 1 Bit
Q+
Q–
R
S
R-S Latch
Resetting
1
0
1
0
0
1
Setting
0
1
0
1
1
0
Storing
0
0
!q
q
q
!q
Bistable Element
Q+
Q–
q
!q
q = 0 or 1

## Slide 69: 1-Bit Latch
D Latch
Q+
Q–
R
S
D
C
Data
Clock
Latching
1
d
!d
!d
!d
d
d
d
!d
0
Storing
d
!d
q
!q
!q
q
0
0

## Slide 70: Transparent 1-Bit Latch
  When in latching mode, combinational propogation from D to Q+ and Q–
  Value latched depends on value of D as C falls
C
D
Q+
Time
Changing D
Latching
1
d
!d
!d
!d
d
d
d
!d

## Slide 71: Edge-Triggered Latch
  Only in latching mode for brief period
    Rising clock edge
  Value latched depends on data as clock rises
  Output remains stable at all other times
Q+
Q–
R
S
D
C
Data
Clock
T
Trigger
C
D
Q+
Time
T